## Slide 2
What is Wifite?
Wifite is a suite of programs we’ll be using to crack the password of a wifi network today.
Wifite is a tool to audit WEP or WPA encrypted wireless networks. It uses aircrack-ng, pyrit, reaver, and tshark to perform the audit.
The tools have been crafted to be automatable with few arguments, and are safe to have run with minimal supervision.

## Slide 3
The Attack
The wifite suite will be used to execute a deauthentication attack against a connected user.
After disconnecting the target machine, it will attempt to
re authenticate with the router, attempting a handshake as part of this process.
Wifite then captures this handshake, and the password hash its handing off, and cracks it, allowing us to get the wifi password from the handshake.
Notably the first part of this attack alone, can be used to jam wifi, but deauthentication attacks are usually a precursor to a bigger attack, like we’re performing.

## Slide 4
The Attack Visualized

## Slide 5
The Attack Visualized

## Slide 6
The Attack Visualized

## Slide 7
Demo Preview
OS: Kali
Tool Name: Wifite
Syntax: sudo wifite -mac --no-pmkid --dict …. kill

## Slide 8
Demo Preview

## Slide 9
Demonstration

## Slide 10
Demonstration Summary
Used software available on the internet to obtain the password to a wifi connection that was “secured”.
Total cost of extra equipment (>$100)
Hours of computer programming, hacking the mainframe, reverse engineering and quantum superpositioning? 0
Total time on Youtube: 7 minutes.
What damage can be done?
Wifi access = Network Mapping (See)
Traffic Monitoring (Sniff)
Vulnerability Scanning (Prod)
Access (Attack)
Persist (Dig in)

## Slide 11
Mitigation
Since Wifite turns off network components and then turns them back on using a handshake based on MAC addresses mitigation is crucial.
Configuration
Segregate LAN, and Guest Network
Utilize Network Switches
Wireless Intrusion Prevention System (WIPS)
Virtual Local Access Network (VLAN)
MAC address filtering rules on firewall
WPA3 for LAN, and Guest Network

## Slide 12
LOD Security team in order of appearance:
Nickolas Garcia (@BlackHat_Manta)
Brendan Boynton (@Brainihack)
Ifedapo Ebiesuwa (@Captain_C0de)
Erik Bjella (@BizzaroWare)
Tony Ayala (@Flex_Luthor)